Name:									Period:		Date:

Electric Circuits problems 3

| SERIES | PARALLEL |
| --- | --- |
| V=V1+V2+V3 | V=V1 =V2=V3 |
| I=I1=I2=I3 | I=I1 + I2+ I3 |
| R=R1+R2+R3 |  |

I. Simplify the following electric circuits. Show your work to get full credit.

1. A 9.0 V battery was recharged with a current of 1.2 A in 1.8x104 s. How much charge was transferred during that time?

A. 1.1x101C

B. 2.2 x104C

C. 1.6x105C

D. 1.9x105C

2. Which of the following correctly labels arrows 1 and 2 and polarities X and Y in the circuit below?

3. Which of the following graphs illustrates Ohm's law?

4. Current is a measure of

A. the number of charges stored in a cell.

B. the amount of energy given to a charged object.

C. the charge passing a point in a circuit in a given time.

D. the resistance to the flow of charged particles in a circuit.

5. Which of the following relationships correctly applies to the circuit shown below?

6. In the following circuit, what is the magnitude of the potential difference between X and Y ?

7. A potential difference of 12 V causes 0.35 C of electric charge to pass through a resistor in 2.6 s. What power does the resistor dissipate?

A. 1.6 W		B. 4.2 W		C. 11 W		D. 89 W

8. The headlights in a car use 95 W of power. A driver parks her car but leaves the lights on. The 12 V battery has 3. 4 ×105 C of stored charge. How long does it take for the battery to lose its charge?

A. 1.1 ×103 s	B. 3.6 ×103 s	C. 4.3 ×104 s	D. 2.7 ×106 s

9. Which of the following household electrical appliances has the greatest rate of energy consumption? (Think Power)